## Slide 1: ECE 445S Real-Time Digital Signal Processing Lab Spring 2023 Infinite Impulse Response Filters
Prof. Brian L. Evans and Dan Jacobellis
Dept. of Electrical and Computer Engineering
The University of Texas at Austin
Lecture 6 http://users.ece.utexas.edu/~bevans/courses/realtime

## Slide 2: Outline
Comparison to FIR filters
  Moving average vs EWMA
IIR biquad filter structures
IIR filter design
Applications
  Chromagram
  Vocoder


X
O
O
X
IIR
FIR

## Slide 3: Discrete-Time Moving Average
  Frequency response:
  Group Delay:

## Slide 4: Discrete-Time Moving Average

## Slide 5: Discrete-Time Moving Average
Group delay:

## Slide 6: Exponential Moving Average
  Frequency response:
Notes: ℎ[𝑛]=〖0.9〗^𝑛 𝑢[𝑛]
𝐻(𝑧)=1/(1−0.9𝑧^(−1) ), |𝑧|>0.9

## Slide 7: Exponential Moving Average

## Slide 8: Exponential Moving Average

## Slide 9: Discrete-Time IIR Filters
How to implement IIR filters?
  Output of LTI system is convolution with impulse response
  Impulse response is infinite in duration
  Cannot directly compute convolution sum
  Instead, use feedback to recursively compute the output

## Slide 10: Many Equivalent Representations
Difference equation

x[n]
y[n]
Unit Delay
0.9
y[n-1]
Pole at
Transfer function
  Assumes LTI system
Poles and zeros in z-plane
Recursive computation requires . For the filter to be LTI, .
Block diagram

## Slide 11: General Form of IIR Filter
  Feedback terms are subtracted so that correspond to denominator coefficients and correspond to numerator coefficients in transfer function

## Slide 12: First Order IIR filter
  Single zero at and a single pole at
  If coefficients are real, pole and zero locations are limited to real axis in the z-plane

x[n]
y[n]
x[n-1]
b1
b0
Unit Delay
-a1
y[n-1]
Unit Delay
Notes: First order filter demo using matlab filterDesigner
Design method: IIR Butterworth Specify order 1
Units: normalized
Wc: 0.1
Design filter
Click pole-zero tab on left sidebar
Select poles and zeros and adjust magnitude
DSP first demos
https://dspfirst.gatech.edu/chapters/08feedbac/demos/3_domain/index.html

## Slide 13: Second Order (Biquad) IIR Filter
Biquad: short for biquadratic
  Transfer function is ratio of two quadratic polynomials
Direct form I
-
-

## Slide 14: Biquad in Direct form II
All-pole IIR Filter
x[n]
v[n]
FIR Filter
y[n]
All-pole IIR filter
FIR Filter
-
-

## Slide 15: Second Order (Biquad) IIR Filter
  Example: bandstop filter
Biquad poles and zeros
  If coefficients are real, then poles and zeros will be complex conjugate pairs
  Allowing complex poles and zeros provides more flexibility for designing filters compared to single order IIR filter

## Slide 16: Vocoder
  Instead of representing speech by signal amplitude, represent based on filter parameters
“Voice Encoder”
  Originally developed for speech synthesis and for encoding speech for telecommunications
  Video: speech synthesis (1939)
  Use as a musical effect (lab #7)
Source-Filter model of speech production
  Opening and closing of vocal folds produces many harmonically related frequencies
  Model vocal tract (including lips, teeth, etc) as LTI filter
  Poles are especially important since they model resonances

## Slide 17: Chromagram
Map audio signal to notes
  Musical notes are perceived as similar when their frequencies differ by an octave (factor of 2)
  12-tone equal temperament divides each octave into 12 bins:
  {C, C♯, D, D♯, E , F, F♯, G, G♯, A, A♯, B}
  MATLAB code (PDF, piano.wav)
Use bank of IIR filters to extract each note
  IIR filters provide much better frequency selection than FIR
  Less delay on average compared to FIR
  Only average energy is displayed, nonlinear phase is okay

## Slide 18: IIR Biquad Frequency Responses
Magnitude response
  Zeros z0 & z1 and poles p0 & p1
  |a – b| is distance between complex numbers a and b
  |ej – p0| is distance from point on unit circle ej and pole p0
IIR Biquad Filter Structures

## Slide 19: Frequency Response?
zeroAngle = 15*pi/16;
z0 = exp(j*zeroAngle);
z1 = exp(-j*zeroAngle);
numer = [1 -(z0+z1) z0*z1];
r = 0.9;
poleAngle = pi/16;
p0 = r * exp(j*poleAngle);
p1 = r * exp(-j*poleAngle);
denom = [1 -(p0+p1) p0*p1];
%%% Normalize the DC response
%%% to 1 in linear units by
%%% setting H(z) evaluated
%%% at z = 1 to be 1
C = (denom * [1 1 1]’) / (numer * [1 1 1]');
freqz(C*numer, denom);
Re(z)
Im(z)
X
O
O
X
Re(z)
Im(z)
O
O
X
X
zeroAngle = pi/4;
z0 = exp(j*zeroAngle);
z1 = exp(-j*zeroAngle);
numer = [1 -(z0+z1) z0*z1];
r = 0.9;
poleAngle = pi/4;
p0 = r * exp(j*poleAngle);
p1 = r * exp(-j*poleAngle);
denom = [1 -(p0+p1) p0*p1];
%%% Normalize the DC response
%%% to 1 in linear units by
%%% setting H(z) evaluated
%%% at z = 1 to be 1
C = (denom * [1 1 1]') / (numer * [1 1 1]');
freqz(C*numer, denom);
Re(z)
Im(z)
O
O
X
X
zeroAngle = pi/4;
rz = 1/0.8;
z0 = rz*exp(j*zeroAngle);
z1 = rz*exp(-j*zeroAngle);
numer = [1 -(z0+z1) z0*z1];
r = 1/rz;
poleAngle = pi/4;
p0 = r * exp(j*poleAngle);
p1 = r * exp(-j*poleAngle);
denom = [1 -(p0+p1) p0*p1];
%%% Normalize the DC response
%%% to 1 in linear units by
%%% setting H(z) evaluated
%%% at z = 1 to be 1
C = (denom * [1 1 1]') / (numer * [1 1 1]');
freqz(C*numer, denom);
Lowpass, highpass, bandpass, bandstop, allpass, notch?
Poles have radius r Zeros have radius 1/r
Zeros are on the unit circle
handout

## Slide 20: Demonstrations
DSP First, 2nd ed., ch. 10
  IIR filtering tutorial (Link)
  Connection between the Z and frequency domains (Link)
  Time/frequency/z domain movies for IIR Filters (Link)
link
IIR filter with one pole and a zero at the origin
Movement of Poles
IIR Biquad Filter Structures